Documentation for AA.XTK    by Ted Eyrick  Compuserve  72446,317
 
Application:
 
    This program is only useful if you are using a Hayes 1200B modem
and Crosstalk XVI.
    When used together it automatically sets up the Hayes 1200B modem to
answer the telephone on the second ring.  It also performs several
more functions:
 
              * Setup the screen colors
              * Setup the greeting message
              * Setup the Password
              * Setup function key assignments for BYe,QUit,XDos
 
Usage:
 
    The  AA.XTK program should be copied to the same diskette or
drive and directory as your Crosstalk XVI program.
    To automatically answer the telephone if you are NOT already in
Crosstalk use the following command:
 
          XTALK AA <enter>
 
The notation <enter> means press the enter key.  Depending upon your
specific system you may have to issue commands prior to the one above
in order to be able to access your Crosstalk program, for example to
change to the proper drive and/or directory.
    To automatically answer the telephone if you are already in
Crosstalk use the following command:
 
             LO AA <enter>
 
The notation <enter> means press the enter key.
    To exit easily the following combined keystrokes enable the three
exit choices of Crosstalk XVI:
 
         Keystroke Combination     Crosstalk Exit Command
             <Ctrl><F1>                BYe
             <Ctrl><F2>                QUit
             <Ctrl><F3>                XDos
 
Performance:
 
    On my IBM PC/XT it takes approximately 8 seconds to get into
Crosstalk XVI and setup the auto-answer mode.  If I am already in
Crosstalk XVI the setup process takes about 4 seconds.
 
Preset Parameters:
 
    You may change any of the preset prarmeters in the AA.XTK program
by using a program editor and following the instructions in the
Modification section. DO NOT USE CROSSTALK XVI TO MODIFY THESE PARAMETERS
BECAUSE THE AUTOMATIC SAVE PROCESS WILL CAUSE THESE PROGRAMS TO FUNCTION
IMPROPERLY.
You may have to refer to your Crosstalk XVI manual for the meaning and
available options for some of the following parameters.
 
            Parameter     Preset Selection
(Greeting)  NAme          Hello!  Please enter your Password
(Access)    ACcept        Creates
(Hardware)  POrt          1
(Password)  PWord         AA
            PArity        None
            DAta          8
            SPeed         1200
            STop          1
 
The last four preset parameters will probably not need to be changed,
but the POrt parameter must match your system.  If your modem is
installed as COM1 then the POrt must be 1 and if your modem is COM2
then the POrt parameter MUST BE CHANGED to 2 .
 
Modifications to AA.XTK
 
    To make these program modifications you must be familiar with at
least the DOS program editor EDLIN.  I suggest that you begin any of
the following modifications by first printing the AA.XTK program so that
you can easily plan your changes.
    To Change the Preset Parameters:
         The preset parameters are found at the following line numbers:
 
    Line Number     Parameter
        1            NAme
        2            ACcept
        17           POrt
        18           PWord
        25           PArity
        26           DAta
        30           SPeed
        31           STop
 
    To Change the Colors:
         The color commands are found on lines  75,76, and 77. You
should refer to your Crosstalk XVI manual for the meaning of the
color command syntax.
 
Contribution:
 
    If this is of value to you please send a contribution to:
 
              Ted Eyrick
              P.O. Box 160307
              San Antonio, Texas 78280
 
    Copyright (C) 1984   All Rights Reserved
 
 
Crosstalk XVI is a product of Microstuf, Inc.
Hayes 1200B is a product of Hayes Microcomputer Products, Inc.