NEWKBIOS

NEWKBIOS.COM is a simple method to activate the F11 and F12 keys on the
IBM enhanced keyboard.  It works by capturing all of the old keyboard
calls and sending them through the new BIOS routines.  The resulting scan
codes are then translated back to match the old keyboard (where
necessary), except for the F11 and F12 keys which are passed untouched.
NEWKBIOS does not replace the BIOS in your computer, it simply redirects
the function calls made by your applications.

After NEWKBIOS is installed, you should see no difference in the operation
of your computer.  Every key and function should act exactly the same as
it did before NEWKBIOS.  The only difference is that your applications
will see eight new scan codes for the F11 and F12 keys (one code for each
shift state).  If you have an application which allows you to redefine
your keys according to their scan codes, then NEWKBIOS will be of use to
you.  If, instead, your application specifies its keys as F1, F2, etc,
then NEWKBIOS will probably do you little good, since your program will
not be able to equate the new scan codes to any particular key names.
Your program will see the new codes, but will have no use for them and
will ignore them.

The codes returned by the BIOS are as follows:

                Scan codes in decimal (Hex in parenthesis)

        Key        Normal          Shift          CTRL           ALT

        F1         59 (3B)        84 (54)        94 (5E)       104 (68)
        F2         60 (3C)        85 (55)        95 (5F)       105 (69)
        F3         61 (3D)        86 (56)        96 (60)       106 (6A)
        F4         62 (3E)        87 (57)        97 (61)       107 (6B)
        F5         63 (3F)        88 (58)        98 (62)       108 (6C)
        F6         64 (40)        89 (59)        99 (63)       109 (6D)
        F7         65 (41)        90 (5A)       100 (64)       110 (6E)
        F8         66 (42)        91 (5B)       101 (65)       111 (6F)
        F9         67 (43)        92 (5C)       102 (66)       112 (70)
        F10        68 (44)        93 (5D)       103 (67)       113 (71)
        F11       133 (85)       135 (87)       137 (89)       139 (8B)
        F12       134 (86)       136 (88)       138 (8A)       140 (8C)

NEWKBIOS has been tested briefly with a PS/2 model 60 and a PC-AT model
339, both pure IBM.  It has not been tested with any clones, nor any
particular applications, though I have run DisplayWrite/4, Multiplan,
Kedit, and many utilities with NEWKBIOS installed, and found no
difficulties.  It has also not been tested with an XT or PS/2-30, but it
should work on these computers.

NEWKBIOS is smart enough to reject most computers which don't support the
enhanced keyboard, but there may be exceptions.  If NEWKBIOS is installed
on a computer which does not support the enhanced keyboard, the most
likely result is that the machine will appear to lock up (actually it will
be unable to receive any keystrokes).  It is also possible that the
program will reject a computer which does support the new keyboard.  There
is simply no way for me to test every possibility.

NEWKBIOS has no provision to prevent itself from being installed twice.

If NEWKBIOS meets your needs, please feel free to use it.  If not, the
source code is provided.  Good Luck.

                                                  Jim Gilliland
                                                  July 16, 1987