LU is a utility to manipulate "LBR" files generated by the PC-DOS
utility of the same name.  The most common use is to pack a group of
related files into a single .LBR file, for modem transfers or 
for archiving.

LU or an equivelant program is usually required to "unpack" the
software packages available on the Chesapeake Remote Bulletin Board
System.

.LBR files are a special file generated by LU (or whatever) that
contain one or more DOS files, and a simple directory. Whenever an
existing library is changed (files changed or deleted) the library
requires "reorganizing".  More on this below.

LU operation is quite simple.  There are only a few commands.  Each
is described below, and a quick summary can be obtained by running
LU like so:

LU <cr>

OPERATING LU

LU commands, etc are entered on the command line after the program
name.  You must ALWAYS enter a command letter, below, and the name of
an LBR file, followed by file names, if needed:

LU <command> <lbr file name> { <optional filenames> }

For example,

LU T FILE.LBR

Lists all the files contained within the LBR file 
FILE.LBR.

                     L U    C O M M A N D S

All LU commands are a single letter. Only one can be entered
at a time.

A Unpack all files from the library.  This is the same  as 
the E (extract) command,  followed by all the file names. This is 
much easier if all you want to do is remove all the files.


T List all files contained in the LBR file.  Each filename 
is listed, along with the size of the file in bytes, and its 
starting offset within the LBR file.  (The offset is pretty 
useless information, but there it is.)

L Same as T.

E Extract a file from the library.  The file(s) to be 
extracted are entered after the LBR file name.  Each file will be 
extracted, and copied to a disk file of the same name.

U Update a library.  This is also used to create new 
libraries.  File name(s) are entered after the LBR file name, and 
each file is added to the library.  Any file of the same name 
already in the library will be deleted first, otherwise just 
added. Pleas read about reorganizing, below.

If the library file does not exist (creating a new  one) 
then you are asked for the number of new slots for the library. 
"Slots"  means the maximum number of files that the LBR file can 
contain.  The number you enter is rounded up to the next highest 
multiple of four;  this is just a peculiarity of the LBR file 
structure.  It does not hurt anything.  After the new library is 
created, any specified files are added to it.

D Delete a file. The just marks the file within the library 
as "deleted".  The library file will NOT change in size;  it does 
not remove the data contained by the file.  See "reorganization", 
below.

R Reorganize  the library.  All free space  (from  deleted 
files,  or existing files that were Updated) is freed up, and the 
LBR file generally becomes smaller. Should be used after a Delete 
or Update command.  Creates a temporary file called LU$$$$$$.TMP, 
therfore you should not use this file name elsewhere.

                     R E O R G A N I Z I N G

The structure of an .LBR file (described in detail  below) 
is very simple. Because of its simplicity, files that are deleted 
or changed still consume space within the LBR file, which must be 
"squeezed" whenever the library is changed.

Deleteing  a file merely marks the file as "deleted";  it 
does not remove the data contained in the LBR file. Updated files 
are deleted first, and also consume space. Therefore, the library 
must be reorganized. This consists of creating a new library, and 
copying the active files to it,  dropping out all the deleted  or 
changed data.

The  rule  is:  reorganize  after  deleting  a  file,  or 
updating a file that already existed.  If the library runs out of 
slots,  and you want to add more files,  reorganize and specify a 
larger number of slots. You can then add to the library.

Reorganizing never does any harm, in any case.


              L B R    F I L E    S T R U C T U R E

The  LBR  file  is  a disk file that  contains  a  simple 
directory,  followed by all the data contained in the files.  New 
files  are added to the end of the LBR file,  and  the  directory 
entry for each file points to the data,  and contains its length. 
Each directory entry is:

00:file status (0= active, FF= deleted, FE= unused)
01:11 character filename (FCB format)
12:16 bit offset to start of data (in sectors)
14:16 bit data length (in sectors)
16:16 bytes of filler

Since the original program was written in BDS C, all 
offsets and lengths are in multiples of 128  bytes, the CP/M 
"sector  size".  LU multiplies these values by 128 before using. 
(Also, all file sizes are rounded up to the nearest 128 bytes.)

The offset is the location of the data for the file, 
relative to the start of the LBR file.

The first directory entry is the directory itself.  The 
filename is always blank, the offset is not used, and the length 
is the length of the directory. Since the length is a multiple of 
128, LU rounds up the number of slots when creating a new .LBR 
file to a multiple of four. (32 bytes per entry * 4 == 128).

                    P E C U L I A R I T I E S

There are only two peculiarities (nice way of saying 
"bugs") that I know of: Filenames without extentions, like "FILE" 
instead of "FILE.EXT" should be entered without a dot.  Entering 
with a dot will cause "NOT FOUND" errors to be generated.  (I.e. 
use "FILE" not "FILE.".  Two, not really a bug, but a side effect 
of the original design: all files are rounded up to the nearest 
128 bytes.  This does not matter for most files, but some, like 
spreadsheet files, will not work unless the size is exactly 
right.  LU (or equivalent) cannot be used with such files. Try it 
and see what happens.

rrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrrr