ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º USING MICROSOFT(R) WINDOWS versions 1.01, 1.03, 2.0 º
     º AND THE HEWLETT-PACKARD DESKJET PRINTER             º    2/22/88    -1-
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
      Microsoft and MS are registered trademarks of Microsoft Corporation.

     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º INTRODUCTION º
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
     The instructions in the following sections will help you to do the
     following:

          1. Install/copy the printer driver file from this disc to your
             MS Windows program disc.
          2. Set up your software package so that it will work correctly
             with the Hewlett-Packard DeskJet Printer.
          3. Be aware of any special feature information or hints for
             using your software package with the DeskJet Printer.

     If you are confused regarding the meaning of "printer driver", refer
     to Chapter 3 in the DeskJet Printer Owner's Manual.

     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º SETTING UP MS WINDOWS º
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
     When using MS Windows to print documents, it is necessary to have a
     copy of the DeskJet printer driver file (DESKJET.DRV) installed on
     your Program Disk. This file is used by MS Windows to correctly acti-
     vate the printer.
     
     A. INSTALLING THE DESKJET PRINTER FROM MS WINDOWS
     
     The following information describes how to use the CONTROL.EXE program
     to install your printer driver.

            ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     NOTE   "Select", as used in the following instructions, means to use
     ßßßß   a mouse or keyboard to choose (or enable) designated menus 
            and/or menu items.
            ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

          1. Start the MS Windows program.
          2. Select the CONTROL Program (CONTROL.EXE) from the MS DOS Exec-
             utive screen.
          3. Select ADD NEW PRINTER under the INSTALLATION menu.
          4. Enter the drive and directory where the DESKJET.DRV printer 
             driver file is located.  For example, if the printer driver 
             is on the DeskJet Printer Driver Disc in drive A, then enter
             A:\WINDOWS.
          5. Press the Enter key or select OK.
          6. Select the HP DESKJET printer driver, then press Enter or
             select ADD.
          7. Select the desired option for copying the driver to your 
             Windows directory.

          
      MS Windows & DeskJet                                      2/22/88    -2-
     ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

         To Select the Printer Output Port:
          
          8. Select the SETUP menu.
          9. Select CONNECTIONS.
         10. Select the HP DESKJET printer.
         11. Select the port to which your printer is connected (usually
             LPT1 for parallel or COM1 for serial).
         12. Select OK or press the Enter key.
 
         If you are using the Serial Printer Port:
 
         13. Select the SETUP menu.
         14. Select COMMUNICATIONS port.
         15. Select the serial port your printer is connected to (COM1: or
             COM2:), then the settings as listed below:
     
             Baud Rate:     9600
             Word Length:   8
             Parity:        None
             Stop Bits:     1
             Handshake:     Hardware
              
         16. Press Enter or select OK.
      
         To select the default system printer and change printer features:

         If you have more than one printer installed, MS Windows allows you
         to choose any one of the printers to be the current (default)
         printer. The current printer is the printer that applications
         designed to run with MS Windows will use. Once you have selected 
         the HP DeskJet printer as the default system printer you may 
         specify the font cartridge and the graphics density.

         17. Select the SETUP menu.
         18. Select PRINTER.
         19. Select HP DESKJET.
         20. Press Enter or select OK.
         21. Use the mouse or keyboard keys to select the cartridge(s) and
             graphics density you want to use with your printer, then
             press Enter or select OK when you're done.  To select two font
             cartridges, follow the instructions below:

             MOUSE METHOD TO SELECT TWO FONT CARTRIDGES
             1. Select one of the desired font cartridges (e.g., A:Courier).
             2. Hold down the Shift key and move the mouse to an additional
                font cartridge (e.g., C:Letter Gothic).
             3. Select/click on the additional font cartridge.
             4. Let go of the Shift key. Both font cartridges should now be
                highlighted (e.g., A:Courier and C:Letter Gothic).
             5. Select OK or press Enter.

             KEYBOARD METHOD TO SELECT TWO FONT CARTRIDGES
             1. Use the arrow (cursor) keys to highlight one of the desired
                font cartridges.

          
      MS Windows & DeskJet                                      2/22/88    -3-
     ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

             2. Hold down the CTRL key and use the arrow (cursor) keys to 
                move to the desired cartridge. Let go of the CTRL key.
             3. Press the space bar. Both font cartridges should now be
                highlighted.
             4. Press Enter.
             
             Refer to the Microsoft Windows Printer Features Table (shown
             below) for a complete list of available fonts and graphics
             densities.

     B. USING PRINTER FEATURES

        Do not use the bottom 1/4" of the page when using MS Paint. Doing 
        so will cause the image to be printed onto two pages.

        Landscape is only used for graphics output.

     ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
     ³                MICROSOFT WINDOWS PRINTER FEATURE TABLE                 ³
     ³                                                                        ³
     ³ NOTE:  All of the fonts listed below include the following features;   ³
     ³ ßßßß   Bold, underline, super/subscripts, multiple columns, strike-    ³
     ³        thru, and 75/150/300 dpi (dots per inch) graphics.              ³
     ÆÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
     ³ DeskJet   ³  Font/Typeface        ³   Point   ³ Italics ³ Proportional ³
     ³ Cartridge ³  & Pitch              ³   Sizes   ³         ³ Spacing      ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³ Internal  ³ Courier 5,10,16.67,20 ³    6,12   ³         ³              ³
     ³ HP22706A  ³ Courier 10,20         ³    6,12   ³   YES   ³              ³
     ³ HP22706B  ³ Prestige Elite 6,12,24³    5,10   ³   YES   ³              ³
     ³ HP22706B  ³ Prestige Elite 8.34,  ³  3.5,7    ³         ³              ³
     ³           ³         16,67,33.34   ³           ³         ³              ³
     ³ HP22706C  ³ Letter Gothic 6,12,24 ³    6,12   ³   YES   ³              ³
     ³ HP22706C  ³ Letter Gothic 8.34,   ³ 4.75,9.5  ³         ³              ³
     ³           ³         16.67,33.34   ³           ³         ³              ³
     ³ HP22706D  ³ TmsRmn                ³ 4,5,8,10  ³   YES   ³     YES      ³
     ³ HP22706E  ³ TmsRmn                ³    6,12   ³   YES   ³     YES      ³
     ³ HP22706F  ³ TmsRmn                ³    7,14   ³   YES   ³     YES      ³
     ³ HP22706G  ³ Helv                  ³ 4,5,8,10  ³   YES   ³     YES      ³
     ³ HP22706H  ³ Helv                  ³    6,12   ³   YES   ³     YES      ³
     ³ HP22706J  ³ Helv                  ³    7,14   ³   YES   ³     YES      ³
     ³ HP22706M  ³*Presentations 3.25,   ³    9,18   ³         ³              ³
     ³           ³         6.5,13        ³           ³         ³              ³
     ³ HP22706M  ³*Presentations 4.05,   ³    8,16   ³         ³              ³
     ³           ³         8.1,16.2      ³           ³         ³              ³
     ³ HP22706M  ³*Presentations 5,10,20 ³    7,14   ³         ³              ³
     ³ HP22706P  ³*TmsRmn                ³ 4,5,6,7,8,³   YES   ³     YES      ³
     ³           ³                       ³ 10,12,14  ³         ³              ³
     ³ HP22706Q  ³*Helv                  ³ 4,5,6,7,8,³   YES   ³     YES      ³
     ³           ³                       ³ 10,12,14  ³         ³              ³
     ÃÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
     ³ *  These cartridges contain only the ASCII character set.              ³
     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾