PRO-SET
                  An IBM Proprinter Configuration Utility
                      Version 3.0 - February 21, 1986

                             by Fred Willshaw
                                207 Oak Lane
                                Cranford, NJ  07016
                                CIS 73075,321

PRO-SET is a utility program which may be used to send control strings to the
IBM PROPRINTER, without the necessity of exiting the program you are currently
using.  It is distributed at no cost and may be freely copied and used.
Should, however, you alter the program code in anyway it is forbidden to pass
this program on to others.  If you would like to see modifications to the
current program please contact the author.

I will attempt to keep the current version on the following Bulletin Boards in
the New York/New Jersey area.  The program will be named PROSETxx.ARC where xx
will indicate the latest version number.

                 Bulletin Board          Telephone#
               ------------------      --------------
               The POLICE              (201) 963-3115
               CFONJ                   (201) 486-2956
               The GOD'S               (201) 277-6522
               Omegammon               (201) 653-3893
               The BOSS                (201) 568-7293
               Wolves Den              (212) 874-6319
               Invention Factory       (212) 431-1194
               Manhattan South         (212) 432-7288 
              
You may either execute the program as a stand-alone DOS batch program or you
may load it into resident memory.  Both modes are accomplished by placing the
desired parameter(s) after the program name, then executing the program. These
optional parameters are:

                  PRO-SET [R=x C=x V=x K=x S=x D=xyy]

Where R=x indicates the type run you wish to perform, the two options are:

           "R" for Load into low memory and remain resident.  The program
               may be accessed by depressing the Hot-Key/Control-Key
               combination you assigned, simultaneously.  This is the default.
	   "B" indicates that you want to run as a batch DOS job and not
               remain resident.  You may also use this option even if the
               program is currently resident.

Where C=x indicates the Color mode you wish to use, the two options are:

           "C" for use the IBM C/G Adapter colors. This is the default.
           "N" for no colors, the NO COLORS option is primarily for users
               of Amber and Green High Res monitors.  Note that if you are
               using a Monochrome Adapter the program will automatically
               detect this.

Where V=x is the Sound On/Off indicator for the program, the two options are:

           "Y" to get Sound warnings of input errors and invalid Drive/
               Path/File Names during the Font Load procedure.  This is the
               default.
           "N" for no sound.

Where K=xx indicates the Hot-Key to be used along with the Control-Key
           key(s) to activate the Memory Resident version.  Enter the
           hexidecimal scan code value.  A partial list is shown below:

           KEY  SCAN      KEY  SCAN     KEY  SCAN     KEY  SCAN     KEY  SCAN
           =========      =========     =========     =========     =========
            A    1E        G    22       L    26       Q    10       V    2F
            B    30        H    23       M    32       R    13       W    11
            C    2E        I    17       N    31       S    1F       X    2D
            D    20        J    24       O    18       T    14       Y    15
            E    12        K    25       P    19*      U    16       Z    2C
            F    21                    * = default

Where S=xx indicates the Control-Key key(s) to be used along with the
           Hot-Key to activate the Memory Resident Version.  Enter the
           hexidecimal total value from the following table, always enter
           as a two digit value:

                  KEY       VALUE TO ADD       EXAMPLE (using the Default)
              ===========   ============       ===========================
              Right Shift        01                           CTRL  04
              Left Shift         02                           ALT   08 
              CTRL               04                                 ==
              ALT                08                Enter total -->  0C

Where D=xyy indicates the physical location of the drive letter you are
            entering.  This is used to allow you to set the internal drive
            configuration to reflect your system's configuration.  The
            following table shows the default values, always enter the
            physical location as a two digit value:

             Drive Letter           Drive Type        Physical Location
             ============           ==========        =================
                  A                 Floppy                   00
                  B                 Floppy                   01
                  C                 Hard Disk                80
                  D                 Hard Disk                81
                  E                 Hard Disk                82
                  F                 Hard Disk                83
                  G                 Hard Disk                84
                  H                 Hard Disk                85
                  I                 Hard Disk                86
                  J                 Hard Disk                87

            An example of using this parameter:  You have three floppy drives
            A-C.  In order to make floppy drive C recognizable by the program
            you would enter D=C02.  In this example the internal drive table
            would be updated to search floppy drive 02H instead of hard disk
            drive 80H when you request data from drive C.  This parameter is
            required since the program uses the BIOS Interrupt 13H instead of
            the DOS service interrupt 21H.
  
                            Installing Pro-set
                            ------------------

In order to install the program, have PRO-SET.COM in the root library or a
sub-directory in the PATH command. Then include the line PRO-SET, along with
your parameter(s) in your AUTOEXEC.BAT file or issue the DOS command PRO-SET
with your requested parameter(s).

When loaded as memory resident , you may then gain access to the program from
any other program by depressing the Hot-Key/Control-Key combination.  The
program will then intercept the keyboard interrupt (09H) and display the
program menu.

                             The Program Menu's
                             ------------------

The first line, [1] LPT1: -- 3:, is used to indicate which line printer port
you want the control information send to.  The default is LPT1:.  If the port
selected is not ready an error message will be displayed.

OPTION    COMMAND FUNCTION                    WHAT HAPPENS
------  --------------------  --------------------------------------------
[A]     Set Condensed Mode    Sends <ESC> 15
[B]     Stop Condensed Mode   Sends <ESC> 18
[C]     Set 12 CPI            Sends <ESC> 58
[D]     Set Emphasized Mode   Sends <ESC> 69
[E]     Stop Emphasized Mode  Sends <ESC> 70
[F]     ONE Direction Print   Sends <ESC> 85 01
[G]     TWO Direction Print   Sends <ESC> 85 00
[H]     Set Double Wide       Sends <ESC> 87 01
[I]     Stop Double Wide      Sends <ESC> 87 00
[J]     Character Set 1       Sends <ESC> 55
[K]     Character Set 2       Sends <ESC> 54 02
[L]     Page Handler/Reset    Displays sub-menu

   [A]  Reset Printer         Sends 24             Empty Buffer
                                    18             Cancel Condensed/Set 10 CPI
                                    <ESC> 45 00	   Cancel Underscore
                                    <ESC> 53 00    Cancel Auto Linefeed
                                    <ESC> 55       Select Character Set 1
                                    <ESC> 61 00 00 Clear Download Buffer
                                    <ESC> 65 12    6 Lines to Inch
                                    <ESC> 67 66    Set 66 Lines to Page
                                    <ESC> 67 00 11 Set to 11 Inches to Page
                                    <ESC> 70       Cancel Emphasized Print
                                    <ESC> 72       Cancel Doublestrike
                                    <ESC> 73       Standard Print Mode
                                    <ESC> 82       Cancel Tab Settings
                                    <ESC> 84       Cancel Sub/Superscript
                                    <ESC> 85 02    Set Bidirectional Print
                                    <ESC> 87 00    Cancel Double Wide Print
                                    <ESC> 95 00    Cancel Overscore
   [B]  Set Top of Form       Sends <ESC> 04
   [C]  Form Length (Inches)  Sends <ESC> 12 00 ## (Where ## is the value
   [D]  Form Length (Lines)   Sends <ESC> 12 ##     is the value you entered)

[M]     1/8" Spacing          Sends <ESC> 48
[N]     7/72" Spacing         Sends <ESC> 49
[O]     Set Normal Quality    Sends <ESC> 73 00
[P]     Set Normal Download   Sends <ESC> 73 04
[Q]     Set NLQ Normal        Sends <ESC> 73 02
[R]     Set NLQ Download      Sends <ESC> 73 06
[S]     Set NLQ Doublestrike  Sends <ESC> 71
[T]     Stop NLQ Doublestrike Sends <ESC> 72
[U]     Load a Font File      Displays sub-menu

   [1]  FONTGEN Created       Indicates that file to be downloaded was
                              created by the FONTGEN program.
   [2]  IBM Format            Indicates that file to be downloaded was
                              created to appear as in the IBM Proprinter
                              Manual page 4-30.

        The next sub-menu is then displayed with which you indicate the
        Drive/Path/Data Set Name of the file to be downloaded.  After
        completion if this sub-menu the file is downloaded to the
        active printer.

Depressing the appropriate key will send the character string and highlight
the option in the menu.  Depressing the <ESC> key will return you to the
Original Program, Pro-Set Main Menu or DOS as appropriate.

                     UPDATES/MODIFICATIONS/CORRECTIONS
                     ---------------------------------

Version 1.1 (01/07/86) - Added support for graphics modes 320X200 and
                         640X200.  Note that this is determined by BIOS
                         Interrupt 10H.  Some programs do not properly
                         set this value, i.e. 1-2-3 in Graphics mode.
                         Since the configuration screen cannot fit in 40
                         column modes, a beep will sound if you attempt
                         to use the program in 40 column mode.

Version 2.0 (01/21/86) - Added support for download fonts.  Depressing
                         option U will present a sub-menu requesting the
                         download font file format.  The first FONTGEN,
                         is created using the FONTGEN utilities found
                         on many Bulletin Boards.  It is well worth the
                         download to get a copy of this program series.
                         The second file format is the IBM standard
                         layout as described in the PROPRINTER Manual.
                         Another sub-menu will be displayed requesting
                         the location and name of the font file to be
                         loaded.
                         A new sub-menu has taken the place of TOP
                         OF FORM.  This is option L and will present a
                         sub-menu offering TOP OF FORM, Form length in
                         inches, Form length in lines and a Reset of the
                         printer.  The Reset is taken from the Technical
                         Reference Manual and issues an interrupt 17H
                         with AH set to a 1.  This option does not seem
                         to work on my Proprinter and as there is no
                         discussion in the Proprinter Manual of such a
                         feature, your helpful assistance is requested.
                         When changing the LPTx: option the selected
                         printer is now checked to ensure that it is
                         online.  If the printer is not available, i.e.,
                         turned off or offline, the program will notify
                         you when selecting the printer.  However, if
                         you are sending a command string and the printer
                         is unavailable, the program will sit patiently
                         and wait for you to turn on the device.

Version 2.1 (01/27/86) - Moved save of current path, FCB and DTA to Font
                         routine in order to speed up execution for 
                         non-font requests.

Version 3.0 (02/21/86) - Added ability to run as a batch program.  Allowed
                         selection for color or black/white for users of
                         amber/green high res screens.  Rewrote documentation.
                         Added screen to show how parameters are entered in
                         the event they are incorrectly entered. Converted
                         all DOS Interrupt (21H) calls to ROM BIOS calls
                         as the DOS calls were destroying the DOS stack
                         when called from a resident program.  See the small
                         print in the DOS manual !  Added ability to turn
                         sound on and off.  Fixed cursor mode on Monochrome.
                         Added ability to select the Hot-Key Combination to
                         activate the memory resident version.  Gave ability
                         to run as a DOS batch program.  Changed Printer
                         Reset routine to pass individual parameters.  Added
                         ability to set the internal drive table to specific
                         configuration requirements.