VPRINT
     Command
     
     --------------------------------------------------
     Purpose: Creates a "virtual printer" by redirecting
              all printer output to a disk file.
     
     Format:  VPRINT [filespec] [/N]
     
     Type:    Internal  External
                          ***
     
     Remarks: Printer output is redirected to the
              specified file, or if none is given, to
              VIRTUAL.PRN.  To avoid overwriting
              existing data, no redirection occurs if
              the file is already in the directory. 
              Output is buffered up until a sector's
              worth of data is available.  
     
              The command VPRINT /N cancels redirection
              and flushes the buffer to disk.
     
              The primary intended use of VPRINT is
              the simplified creation of formatted DOS  
              files from Easywriter.  By printing to
              disk, it is not necessary to manually add
              end of paragraph markers at the end of     
              each line, or to use the Easywriter    
              utility TRANSFER.
     
     Note:    VPRINT is still in an experimental form.
              Use of the PrtSc key while redirection
              is in effect will cause a system crash.    
              On the author's 64K system, a single 5
              digit number overwrites five charactors    
              near the beginning of any file loaded by
              Easywriter.  This overwrite can be
              corrected with the editor prior to
              printing.
     
              Developed by David Whitman