Screen Save Program for the Hercules Graphics Card

There is in circulation on electronic bulletin boards, magazines and
users groups a program called variously, Mono Blank, Monitor Blank,
MONBLK2, SCRNSAVE, and probably a few other things by now too. The
program is designed to remove the display from the monochrome screen
after some period of inactivity. This is meant to protect the monitor
from having an image burned into the phospher if something is left on
the screen for a long time. These programs will work on IBM's
monochrome board, but are quite unsuitable for use with a monochrome
graphics card. This is because in graphics mode the 6845 CRT controller
chip is operating with a different set of controlling parameters than
it uses in text mode. If one of these programs goes into effect while
the board is in graphics mode it will remove the display but not
replace the proper parameters, and quite severe monitor damage can
result.

On this diskette is a file called HGC.COM. It is an elaboration of the
HGC.EXE file that has been shipped with the Hercules Graphics Card
model GB101. The program will blank the screen after there has not been
any activity at the keyboard for five minutes. It will only run
properly on the Hercules Graphics Card, do not use this program with a
regular IBM Monochrome Display/Printer Adapter Card or any video
adapter other than the Hercules Graphics Card. If you are using any
other version of this program with a Hercules Graphics Card you should
get rid of it immediatly, and tell anyone else that you know who may be
using it in the same situation to do so as well. This program was
written by Hercules in response to a number of their customers who were
having unfortunate experiences with other versions of this program.

To use the program simply type: HGC SAVE while at the DOS level. If you
want to incorporate this command into the regular start-up
configuration of the Hercules Card you can specify HGC FULL SAVE or
HGC HALF SAVE. After the program takes effect and blanks the screen the
display can be restored by striking any key. (The shift key is
recommended because the keystroke will be processed.)