TPTIMER - Routines for high-resolution timing of events
-------------------------------------------------------
Brian Foley and Kim Kokkonen
TurboPower Software
6/88
Version 1.0
Released to the public domain

Overview
------------------------------------------------------------------------------
One problem commonly faced when trying to run benchmarks on a PC is that, by
default, the system clock is accurate only to 1/18th of a second. The TPTIMER
unit provides a simple and convenient means of timing events with microsecond
resolution. It does this by reprogramming the timer chip, but the gory details
are hidden from you. TPTIMER automatically reprograms the timer before your
program starts, then restores it to its normal state when your program ends.
Unless your program is working with the timer chip at a very low level, no
incompatibilities should arise, nor should the performance of your program
change.

Using TPTIMER
------------------------------------------------------------------------------
TPTIMER is very easy to use. You just add it to your program's USES statement
and call the ReadTimer function when you are ready to start/stop timing. For a
simple demonstration of how to use TPTIMER, see TTDEMO.PAS.

TPTIMER interfaces the following routines:

  function ReadTimer : LongInt;
    {-Read the timer with 1 microsecond resolution}

  function ElapsedTime(Start, Stop : LongInt) : Real;
    {-Calculate time elapsed (in milliseconds) between Start and Stop}

  function ElapsedTimeString(Start, Stop : LongInt) : string;
    {-Return time elapsed (in milliseconds) between Start and Stop as a string}

  procedure InitializeTimer;
    {-Reprogram the timer chip to allow 1 microsecond resolution}

  procedure RestoreTimer;
    {-Restore the timer chip to its normal state}

The first three of these are probably the only ones you'll ever need to use.
InitializeTimer is executed automatically before your program begins,
RestoreTimer when it ends. You shouldn't call these yourself unless you want
to reset the timer to its normal state temporarily, as you might before using
the Exec procedure in the DOS unit:

   RestoreTimer;
   Exec();
   InitializeTimer;

Limitations
-----------
Because long integers are used to represent time, TPTIMER cannot be used to
time events longer than about 60 minutes:

   4,294,967,295 (= $FFFFFFFF, largest unsigned value represented by longint)
 /     1,193,181 (timer resolution in counts/second)
 ---------------
           3,599
         /    60 (seconds/minute)
         -------
            59.9 minutes

This should hardly be a problem, however, since an event longer than an hour
presumably doesn't need to be timed with 1-microsecond accuracy anyway.

Also note that the process of reading the time takes time. Hence, results of
timing very short events will be skewed by the overhead of reading the timer.
The following table shows the time measured between two calls to ReadTimer,
one right after the other.

  Toshiba 1000 (4.77MHz 8088)    125 microseconds
  ATT 6300 (8MHz 8086)            53     "
  Deskpro 286 (8MHz 80286)        35     "
  Sperry IT (7.1MHz 286, 0 wait)  32     "
  IBM PS/2 model 50               25     "
  PC Designs GV386 (16MHz)        27     "