BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³     BNU Rev 5 FOSSIL Compatible Communications Driver     ³
  ³                       Release v 1.30A                     ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
  
  
           Copyright (C) 1989 David Nugent & Unique Computing P/L
                           All Rights Reserved
  
  
  BNU is a FOSSIL compatible Communications driver, suitable for use
  with the following (among others) bulletin board and FidoNet
  style software:
  
          Fido v11, 12    Tom Jennings, Fido Software
          BinkleyTerm     Vince Perriello, Bob Hartman, Alan
          Applegate,
                          Bit Bucket Software
          Opus-CBCS       Wynn Wagner III, The POLE of Dallas
          QuickBBS        Adam Hudson
          SEAdog          Thom Henderson, System Enhancement
          Associates
          FrontDoor       Joaquim Homrighausen, Interzone
          Software,Inc.
  
  It handles hardware specific aspects of communications, to enable
  the above applications to run in multiple environments which are
  supported by a FOSSIL compatible driver.  BNU is designed for the
  IBM PC, XT, AT 386 under the MS-DOS operating system version
  2.10 and above, OS/2 in 'DOS compatibility' mode and under PC-
  MOS/386.  It may be compatible with other environments which
  emulate MS-DOS, but this has yet to be determined.  You may have
  problems using network cards or other add-on cards which use IRQs
  used by a FOSSIL driver.
  
  BNU can replace both/either Opus!Com (written by Bob Hartman),
  and X00.SYS (written by Ray Gwinn), but differs from them in the
  following respects:
  
          o       BNU has been built to handle up to 16 COM ports
                  concurrently,
  
          o       It has an "open architecture" which will allow is
                  adaptation later in its development to support
                  multiport
                  shared interrupt and intelligent asynchronous IO
                  boards,
  
          o       It supports the 16550 USART used in many ATs and
                  386 machines in fully buffered mode, providing the
                  capability of much higher baud rates even in
                  multitasking
                  environments,
  
          o       The driver is extremely FAST, optimised for speed,
                  yet takes up very little memory,

                                  - 1 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  
          o       Incorporates an optional "diagnostic" mode, so
                  you (the user) can inspect the state of the
                  FOSSIL driver itself; assisting in debugging and
                  optimisation of software being written to use
                  FOSSIL calls, and in attempting to determine
                  oblems in software using a FOSSIL, such as a
                  mailer or BBS 'door'.  The diagnostics window is
                  keyboard selectable via Ctrl-Shift-(Keypad)5
  
          o       Incorporates built-in support for network and
                  multitasking software, forcing ill-behaved
                  processor intensive programs to give more of
                  their time-slice to the system when inactive or
                  when simply "polling" communications or keyboard
                  functions for activity or status reports.
  
  
  NOTE:   BNU is both a FOSSIL driver (TSR) and a utility which can
          manipulate the resident version of itself.  On first
          successful loading, it  with terminate and leave the
          driver portion of itself (only  about 5K or so) resident,
          and allocate comm buffers for each of the enabled ports
          (typically using 14K for a one port install when
          'diagnostics' mode is enabled).
  
  
  =========
  IMPORTANT
  =========
  
  All versions of BNU will either be BETA TEST versions or full
  releases.  Beta test releases will carry an alphanumeric suffix
  after the version number, both on the distributed archive and
  whenever BNU displays its version number.
  
  Release versions will not have such a suffix.  These will usually
  (but not always) be identical to the last issued beta release
  when found to be a stable and bug free version.  Thus, beta
  version 1.10C - when found stable - would be reissued as version
  1.20.
  
  
  ===============
  PROBLEM REPORTS
  ===============
  
  If you have problems in getting BNU to run on your system,
  remember that I cannot solve that problem if you do not take the
  time to let me know.  If you do decide to pursue any problem,
  please give as much detail regarding your system as possible so
  that I can more readily evaluate why something may or may not be
  occuring.  Please keep the information relevant (ie. I don't need
  to know your shoe size, but I may want to know what's in your
  CONFIG.SYS!).
  

                                  - 2 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  Some information I'll probably need:
  
          o       Machine type/model and class (XT/AT/386 etc.)
  
          o       Type of USARTs installed (8250/16450/16550 etc.)
  
          o       Communcations software you're running
  
          o       Contents of your AUTOEXEC.BAT/CONFIG.SYS or other
                  batch files which may be relevant
  
          o       Switches used to load BNU.COM
  
          o       Whether you've used BNUPORT to change port
                  assignments
  
          o       Brief description of modem if at all unusual ie.
                  high speed, non-standard or sub-standard (don't
                  laugh -mine's in the last category!)
  
          o       Version of MS-DOS in use
  
          o       Multitasker in use (if any), including version
  
          o       Other TSR's loaded during communcations activity
  
          o       What other FOSSIL drivers have worked in the past
  
          o       An accurate and complete (oh, I wish!)
                  description of your problem
  
          o       Contents of a diagnostics window when the problem
                  is occuring (if at all possible)
  
          o       If you have TurboPower's TSR utilities or Andrew
                  Wylie's DOSMAP program (or some similar DOS
                  memory control block mapping utility), then
                  redirect output of this to a test file and
                  include it with your report.  Try to duplicate
                  the exact state of memory when the problem
                  occurs. Something like:
  
                          "mapmem -v -h >output.mem"
  
  
  ============
  USING BNUCOM
  ============
  
  When running BNUCom, avoid using any other software which
  purports to enhance communcations products (such as 16550.EXE). 
  These WILL NOT work, and will can cause your system to crash.
  BNUCom already uses the 16550/16550AN to full advantage
  
  
  

                                  - 3 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  ====================
  COMMAND LINE OPTIONS
  ====================
  
  --------------------------------------------
  Group A:  Available on first time load only.
  --------------------------------------------
  
  
  o       -R:nnnn Set RX (receive) buffer size to <nnnn> bytes
  
  The default RX (receive) buffer size is 4K, or 4096 bytes. In
  practice, only a fraction of this is really used unless the
  software you run likes sleeping for long periods (ie. none that I
  know of).  You can probably lower buffers safely to 512 bytes or
  even less unless using a s-l-o-w machine and a f-a-s-t modem/baud
  rate.  It defaults to 4K only for compatibility reasons.
  
          e.g.   BNU -R:1024      (sets 1K receive buffer)
  
  
  o       -T:nnnn Set TX (transmit) buffer size to <nnnn> bytes
  
  A greater amount of the transmit buffer is used, and this can
  greatly enhance performance in file transfers.  It also defaults
  to 4K.  With slower modems, this can be decrease to about 2K or
  2048 bytes.  On faster modems, this can be increased to the
  maximum block transfer size that your mailer software is able to
  use; which in ZedZap (Opus/Binkley/D'Bridge/FD style) transfers
  is 8K for TB's and HST's.  Generally that size (2K for 2400
  bauders like me) is a good indication of the ideal transmit
  buffer size.  Any size specified is ALWAYS rounded to the next
  paragraph (16 byte boundary) if it is not evenly divisable by 16.
  
          e.g.  BNU -T:8192   (sets 8K transmit buffer)
  
  
  o       -P:nn   Enable nn concurrent ports (1-16)
  
  Up to sixteen ports can be run concurrently.  In the current
  version, the driver code (+ optional diagnostics code) plus 64
  bytes for each port, plus TX and RX buffers for each port cannot
  exceed 64K.  If the situation arises where more than that is
  required, it CAN be changed and extended - if required -up to 64K
  of buffer space per port (but I hardly see the need). BNU
  defaults to one port only (using the miminum amount of memory).
  
          e.g. BNU -P:4    (enables up to 4 ports)
  
  
  o       -D      Enable diagnostics output
  
  This switch enables a diagnostics information block, which is
  placed on the screen.  Information for up to 4 ports can be
  displayed on the screen, overlaying anything currently displayed.
  The diagnostic module is hooked into the timer module via the

                                  - 4 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  timer interrupt, and is refreshed only while the port is active.
  
  You can selectively enable or disable the diagnostics display
  from a keyboard "hot key".  The window is in an initial "on"
  state, but can be toggled on or off by pressing Shift-Ctrl-5 (the
  '5' located on the numeric keypad).
  
  A typical diagnostic display - all values are in Hexadecimal (to
  the base 16).  This information is provided for informational
  purposes only for those interested:
  
  ÚÄÄ Port 0001 ¿ ÄÄÄÄÄÄÄÄÄ Port number, zero based (0=COM1)
  ³ TX Cnt 0001 ³ ÄÄÄÄÄÄÄÄÄ Chrs currently in transmit buffer
  ³ TX Max 003F ³ ÄÄÄÄÄÄÄÄÄ Maximum chrs found in transmit
  ³   Base 141E ³ }          buffer (this is cleared whenever
  ³    Top 241D ³ }ÄÄÄ¿     the port is initialised)
  ³   Next 144A ³ }    ÀÄÄÄÄ Transmit ring buffer pointers/limits
  ³    End 1449 ³ }
  ³ RX Cnt 0000 ³ ÄÄÄÄÄÄÄÄÄ Chrs currently in receive buffer
  ³ RX Max 0019 ³ ÄÄÄÄÄÄÄÄÄ Maximum chrs found in receive
  ³   Base 241E ³ }          buffered (cleared on init)
  ³    Top 341D ³ }ÄÄÄÄÄÄÄÄ Receive ring buffer pointers/limits
  ³   Next 249A ³ }
  ³    End 249A ³ }     ÚÄÄÄÄÄ Flow disabled below this point
  ³ LoWatr 0200 ³  ÄÄÄÄÙ         (XON sent, CTS set high)
  ³ HiWatr 0E00 ³  ÄÄÄÄÄÄ¿
  ³   Flow 0000 ³  ÄÄÄÄ¿ ÀÄÄÄ Flow enabled above this point
  ³   Stat 6008 ³  ÄÄÄ¿³          (XOFF send, CTS low)
  ³ UARTBS 0008 ³ ÄÄÄ¿³³
  ³ Errors 0000 ³ ÄÄ¿³³ÀÄÄÄÄÄ Flags used to manipulate flow
  ³ ErrFun 0000 ³ Ä¿³³³       control:  low bute controls local,
  ³  Calls 5F73 ³ ¿³³³³       high byte remote.  bit 0=XON/XOFF
  ÀBNUCom V1.30AÙ  ³³³³³       asserted, bit 1=CTS/RTS low.  Bit
                   ³³³³³       7 in low byte controls local xmit
                   ³³³³³       status in the USART.  If set, the
                   ³³³³³       transmit buffer is full and cannot
                   ³³³³³       be written to until cleard.
                   ³³³³³
                   ³³³³ÀÄ Contains the current line and modem
                   ³³³³   status flags, as defined in the FOSSIL
                   ³³³³   Rev 5 spec.
                   ³³³³   bit 3=always set
                   ³³³³   bit 7=carrier detect
                   ³³³³   bit 8=receive buffer not empty
                   ³³³³   bit 9=receive buffer overrun indicator
                   ³³³³   bit 13=transmit buffer not full
                   ³³³³   bit 14=transmit buffer is empty
                   ³³³³
                   ³³³ÀÄÄ Indicates the size of your USART's
                   ³³³    internal buffer.  This will be 1 for a
                   ³³³    8250 or 16450, and either 08 or 10 for
                   ³³³    a 16550 or better.
                   ³³³
                   ³³ÀÄÄÄ Errors count; for functions returning
                   ³³     errors.  This should almost always be
                   ³³     zero; it gives an indication of how

                                  - 5 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

                   ³³     many calls an application makes that
                   ³³     the FOSSIL considers "illegal".
                   ³³
                   ³ÀÄ Indicates the FOSSIL function code passed
                   ³   by the application when an error occurred
                   ³
                   ÀÄÄ Accumulated number of FOSSIL calls made.
  
  
  One caution: there is an overhead associated with running the
  diagnostics window - it should be used carefully.  Since it
  steals time during the timer interrupt, it will reduce the amount
  of time that your application actually runs.  This is not too
  noticable under standard DOS (in fact, it is all but invisible),
  but the effect in multitasking systems such as DesqView,
  MultiLink or PC-MOS/386 can be dramatic (use under DoubleDOS is
  not supported).
  
  If you're running your system on an 8088 based system, don't use
  diagnostics: you will have problems unless you are running a
  faster version of that chip.  Alternatively, you should slow the
  refresh rate of the diagnostics window.  As an indication: BNU is
  developed on a 10MHZ AT running no-wait states.  Diagnostics
  works fine on one port, but problems begin to appear on two ports
  (even more pronounced under DesqView), resulting in frequent
  YooHoo failures during mail sessions and the occasional error
  during file transfers. Three ports enabled (that is, three panels
  being updated to the screen) causes almost all mail sessions to
  be unsuccessful.  Best results can be gained by using a 386 at
  16MHZ or better.
  
  This can't be stressed enough:  diagnostics should not be enabled
  as 'standard', but should be used infrequently for optimisation
  or debugging: it slows the driver down significantly.  If you
  want to load diagnostics but have them completely inactive by
  default, use the following sequence:
  
          REM Load diagnostics module when installing BNU
          BNU -D <other switches ...>
          REM Immediately disable them
          BNU -N
  
  The option to load without screen refresh "-Dn-" still uses clock
  cycles: only the screen update is inhibited.  The "-N" switch
  actually disables the background processing and will not cause
  the same degradation in performance.
  
  
  -----------------------------------------------
  Group B:  Available when run NOT on first load.
  -----------------------------------------------
  
  
  o       -U      Uninstall (if already resident)
  
  Detatches the FOSSIL and unloads it from memory. This will only

                                  - 6 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  be allowed when no ports are active on the system. Be sure to
  unload all API's, such as VFOSSIL first.
  
  
  o       -N      Disable diagnostics output
  
  Disable output of diagnostic information to the screen. Handy
  when you get bored of it!
  
  
  o       -D      Reenable diagnostic ouput
  
  This switch (explained in previous section) is only available
  when diagnostics were enabled on first loading, and have
  subsequently been disabled.
  
  
  o       -C      Recapture INT 14H
  
  Takes a look at the current location of INT 14H and makes sure
  that it points to BNU.  If not, it resets the INT 14H address to
  the resident version of BNU.  This switch must not be combined
  with any others!
  
  
  o       -W      Enable/disable carrier watch
  
  This switch enables or disables carrier watch for a particular
  port.  The port nominated need not have been initialised
  previously (this will automatically be done). If carrier while
  the watchdog function is active, the system will be rebooted. 
  Syntax is:
  
          -W:1+   Enables watchdog on COM2 (port 1)
          -W:0-   Disables watchdog on COM1 (port 0)
  
  Ommission of the '+' or '-' is considered an error.
  
  
  
  ----------------------------------------------------------
  Group C:  Available when run either first/subsequent times
  ----------------------------------------------------------
  
  
  o       -H      Display help information
  
  Displays information about command line switches and usage for
  those who don't believe that reading manuals is a very useful
  exercise.  Pity they'll probably never discover or know about
  this switch either unless told. ;-)  This switch must be use
  exclusive of all others.
  
  
  o       -Lp:nnnnn       Lock port <p> baud rate to <nnnnn>
  

                                  - 7 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  nnnnn must be a valid baud rate: one of 300, 600, 1200, 2400,
  4800, 9600, 19200 or 38400.  High speed modems locked at a baud
  rate of 9600 or above also have CTS/RTS hand-shaking permanantly
  enabled.  A baud rate specification of zero "unlocks" the baud
  rate and resets hanshaking to default.
  
  
  o       -M      Enable/disable initialisation message
  
  Normally the driver outputs a message when initialised.  This may
  be suppressed or reenabled by using this switch:
  
          -M1     Suppress initialisation message
          -M0     Reenable initialisation message
  
  
  o       -B      Perform unconditional warm reboot
  
  Required for certain situations where no other graceful method
  exists.  No ports need be active, nor need the driver be
  currently resident.
  
  
  o       -X      Enables support of a multitasking system
  
  BNU will detect most common multitasking software in use, such as
  DesqView, TopView, TaskView, MultiLink and PC-MOS/386.  Some
  multitasking systems are more difficult to detect using software
  methods, and their use must be "forced" by using this option on
  the command line.
  
  Supported multitasking systems are:
  
          0 = Autosense   Assumes none, but tests for one active on
                          the system
  
          1 = AT-BIOS     This is the default for systems
                          supporting the AT-BIOS standard, includes
                          most LAN networks which use some form of
                          multitasking kernel.
  
          2 = TopView
          3 = DesqView
          4 = TaskView
          5 = DoubleDOS   These will be automatically found
                          and the option to force selection is
                          included for completeness only.
  
          6 = Windows     This is valid under Windows/386 only -
                          version 2.01 and above.
                          
          7 = MultiLink   Detected automatically.
  
          8 = PC-Mos/386  Will be implimented more fully in the
                          next release.
  

                                  - 8 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  By default, BNU assumes no multitasking system is present and
  will not attempt any multitasker configuration, even if one is
  installed.  Multitasking options must be specifically enabled
  with this switch (at least -X0).
  
  See the warnings above re: diagnostics mode when using
  multitaskers.
  
  
  o       -F      Enables faster screen writes using ANSI
  
  This switch is used for versions of DOS which support faster
  character output via the INT 29H interface (used to call the ANSI
  driver directly).  To my knowledge, this will work on all DOS
  versions 2.00 thru 4.01 (but since it is "undocumented", there is
  no guarantee that it will work).
  
  
  In the majority of cases, no switches need be used.  In its default
  mode, BNU will support either COM1 or COM2 automatically; whichever
  is required by the application.
  


  
  ===================================================================

  
  "Undocumented Features"
  
  Following are some previously undocumented features (not bugs!) of
  the driver which are either intended for use in batch files or
  similar processing, are non-obvious features of the driver or are
  further explanation.
  
  
  
  INSTALLATION
  ------------
  
  BNU is usually installed in your AUTOEXEC.BAT or at some time
  before you load your communications software.  Alternatively, MS-
  DOS 4.xx has an option to allow loading of some 'compatible' TSRs
  using an "install=" statement in your config.sys.  A major
  benefit of this is that BNU can be loaded before any environment
  variables are set, and so takes up the absolute minimum of RAM. 
  However, when loaded from CONFIG.SYS, BNU cannot be deallocated
  from memory using the "-U" option.
  
  
  
  ERRORLEVELS
  -----------
  
  The following errorlevels are returned by BNU (this also
  documents some of the possible errors which can be returned):

                                  - 9 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  
           1      Never (must be abnormal exit).
  
           2      BNU cannot be loaded because BNU is not
                  the active FOSSIL.
  
           3      Incorrect version of BNU is resident
                  Attempt was made to manipulate a resident driver
                  with a different version of BNU.COM.
  
           4      Can't change while ports are active.  Some
                  command line switches are only valid when the
                  driver is first loaded or when no ports are
                  active (for example, an attempt was made to
                  change buffer sizes).
  
           5      BNU is not yet resident.
                  A command line switch which requires the FOSSIL to
                  be resident was specified.
  
           6      BNU is still active
                  BNU cannot unload from memory when COM interrupts
                  are active.
  
           7      Memory allocation error
                  A serious DOS memory allocation error was
                  returned
  
           8      Invalid command line option
  
           9      Can't deallocate - API active
                  An attempt was made to unload from memory without
                  first disabling active API's (for example, a
                  VFOSSIL driver)
  
          10      Unable to reboot
                  Attempt to reboot failed (from command line
                  switch)
  
          11      Error enabling/disabling carrier watch
                  An inconsistancy was found in attempting to
                  enable or disable carrier watch; either the watch
                  could not be installed or it could not be
                  deactivated (usually by giving an incorrect port
                  number)
  
          12      Error in recapturing interrupt
                  Couldn't recapture INT 14H, even though correct
                  BNU version and BNU was found
  
          13      Cannot unload from memory when loaded from
                  CONFIG.SYS
  
  
  
  INITIALISATION

                                  - 10 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  --------------
  
  The initialisation message is displayed when typing just BNU on
  the command line.  This displays the maximum number of ports
  which can be concurrently active, and the number currently
  active.  This message (also displayed when a COM port is
  initialised from within an application) can be suppressed and
  reenabled with a command line switch.
  
  
  
  MULTITASKERS
  ------------
  
  When multitasker support is enabled, the initialisation message
  also displays the type of multitasker (if any) found to be
  active.  This gets checked EACH TIME a port is initialised, so
  that the correct code will be used, say when BNU is loaded first
  under DOS, then recaptured under DesqView.  When you use other
  than the automatic sensing of the multitasker (-X0 enables
  autosense) with a specific multitasker type (do so at your own
  risk!), no attempt will be made to change it in subsequent
  initialisation calls.  No multitasker specific code is actually
  used until a port is initialised and used (to prevent 'hanging'
  under DoubleDOS for example).  There is no need to specify the
  multitasking system in use on each invokation of BNU.
  
  
  
  MEMORY
  ------
  
  BNU.COM is approximately 8K in size.  It is made up of the
  following main modules:
  
  Description           Size   Used by                Resident
  -------------------------------------------------------------
  ISR Device Driver     0.5K   Common - all ports     Yes
  INT 14H Despatcher    4.4K   Common - all ports     Yes
  Diagnostics Model     0.7K   Common up to 4 ports   Optional
  Initialisation/Setup  1.0K   Run time only          Discarded
  Command line utility  1.6K   Run time only          Discarded
  -------------------------------------------------------------
  
  What eventually remains resident depends upon what command line
  options are used.  Initial over head is about 5K for the ISR and
  despatcher.  If diagnostics are used (rarely), then add 0.7K. Add
  to this, the sum of the transmit and receive buffers times the
  number of communications ports selected.
  
  Due to problems in memory allocation under certain versions of
  MS-DOS, the environment is not deallocated until the driver is
  unloaded from memory, therefore the current used environment size
  must also be added.
  
  An example:

                                  - 11 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

                2 ports
                1024 bytes transmit
                2048 bytes receive
  
    Driver overhead                               4.9K
    Tx & Rx Buffers (1 port) = 3K  * 2 ports      6.0K
    Environment (say)                             0.5K
                                                ------
                              Resident size  =   11.4K
                                                ======
  
  This can of course be tuned to suit, and this is one of the
  primary resons why the diagnostics module was not eliminated
  after completing beta testing.
  
  
  
  THE DIAGNOSTICS WINDOW
  ----------------------
  
  The ability to view the state of the FOSSIL driver is very useful
  when developing software utilising FOSSIL calls.  It can also be
  an invaluable aid in "tuning" the driver to your machine.  Memory
  is precious - especially in a multitasking environment, and most
  of the time, the standard 4K transmit and receive buffers are far
  too much to allocate.  This can only be empirically tested.
  
  Instead of "guessing" and using trial and error to see how well
  the driver performs, it is much better to enable the diagnostics
  window.  This provides a 'snapshot' of the driver 18.2 times per
  second (each clock tick).  Particular fields to look at are:
  
  
      "TX Cnt"    Indicates how full the transmit buffer is
                  in bytes.
  
      "TX Max"    This is the current 'maximum' count if characters
                  in the transmit buffer detected by the diagnostics
                  routine (it views the driver in 'snapshots' so
                  cannot be completely accurate.
  
      "RX Cnt"    Indicates how full the receive buffer is
                  in bytes.
  
      "RX Max"    Maximum count of characterfs in the receive
                  buffer (see TX Max).
  
      "HiWatr"    These are the low and high mark used by
      "LoWatr"    FOSSIL when receiving.  If the receive
                  count constantly exceeds the "HiWatr"
                  value, then you may need to increase the
                  size of your receive buffer.  This event
                  usually triggers the FOSSIL to prevent
                  the other end sending.
  
      "Calls"     Particularly useful for monitoring program

                                  - 12 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

                  activity.  This counter ticks over every
                  time the running application requests a
                  FOSSIL service.
  
      "Errors"    Locates possible problems in the program
                  you are running.  Any time the program
                  makes an "illegal" call (usually incorrect
                  register values).  The last FOSSIL function
                  code invoked which triggered the error will
                  be displayed next to "ErrFun".
  
  
  By observation, it is possible to calculate the optimum size for
  both receive and transmit buffers.  In general, you should be
  more generous with receive buffers.
  
  All values are displayed in hex (sorry!).  If you're unfamiliar
  with this numbering system, then you'll have to learn at least a
  little if you want to use diagnostics.
  
  The diags window may be switched on or off using either a command
  line switch ("-N" for off, "-D" to reenable) or suppress the
  window's refresh using the "hot key" - Ctrl-Shift-Keypad5.  Since
  this window is not a true "popup" (in the sense that it doesn't
  save the screens contents before displaying itself and restoring
  it later and it doesn't stop the foreground task but runs
  concurrently with it), switching off the window will leave it
  displayed until your application next uses and overwrites that
  part of the screen (or it scrolls off).
  
  Some multitasking systems often adjust the number of clock ticks
  (and so timer interrupts) to be different from the 18.2 ticks per
  second standard.  Increasing the tick rate may provide poorer
  performance when diagnostics are on, since a relatively greater
  percentage of time will be taken up servicing the timer and
  displaying the window.
  
  You can aqttempt to get around this problem by giving a numeric
  argument to BNU's diagnostics enable switch.  "-Dn" (where n is a
  number from 0 through 65535) will cause the display to only
  refresh itself every multiple of 'n' ticks.  You can adjust the
  timing by subsequently invoking BNU with a different value for n.
  If a value is not given, BNU assumes zero, and so will refresh
  the window every clock tick.
  
  
  16550 USART SUPPORT
  -------------------
  
  BNU fully supports the 16550 USART in buffered mode.
  
  
  
  THE BNUPORT UTILITY
  -------------------
  

                                  - 13 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  BNUPORT changes port assignments used within the driver.  It
  reads and patches the existing driver file "BNU.COM" to use a
  specific interrupt and/or IO port base address.  It also supports
  setting shared interrupt port values and masks (leave 0 for
  none).
  
  BNUPORT searchs first the current directory, then all directories
  in the PATH for BNU.COM and uses the first one located.  It
  presents a form which may be used to change communcations
  parameters.
  
  It is advisable NOT to change these values unless you know what
  you're doing.  You may find a hardware manual supplied with a
  serial adaptor useful in locating the required values.
  
  Shared interrupt ports are not fully implimented (ie. that
  section of the driver is in beta test).  You would be advised to
  not use that feature until a future version (contact me if you
  are interested and have such a card).  This will provide the
  ability to use DigiCom 4/8 port, Hostess, Stargate, Anvil Brumby
  and Stallion serial adaptor boards (and some others) with the
  FOSSIL driver.
  
  
  
  UNDER DEVELOPMENT ...
  ---------------------
  
  An OS/2 FOSSIL driver based on BNU is currently being written,
  with an OS/2 (and other non-DOS OS's) FOSSIL specification soon
  to be published by me.  I have also embarked on porting
  BinkleyTerm to OS/2, but this may take a few months (subject to
  how quickly the FOSSIL can be implimented).
  
  BNU is currently being restructured to use an alternative far
  call model, instead of the INT 14H interface.  This will follow
  the same lines as the non-DOS FOSSIL interface, and is expected
  to yield significant performance benefits for DOS as well as
  benefits for the developer.
  
  Enquiries regarding this project should be directed to any of the
  electronic addresses below.
  
  
  ==============================================================
  
  LICENSE AGREEMENT
  -----------------
  
  Programs and documentation are supplied free of charge on an as
  is basis to the Fidonet (and othernet) community.  You are free
  to use them in any non-profit venture with no obligation on
  either myself or my company to support or be responsible for any
  such use (or misuse).
  
  BNU, BNUPORT and this documentation is the exclusive property of

                                  - 14 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  Unique Computing Pty Ltd, and is protected by international
  copyright laws.  By obtaining a copy of the package, you do not
  "own" a copy -simply a license to use it.  All property rights
  are retained by the owner.
            
  You may use the package and/or give copies of the package to
  others including posting for download on a bulletin board, but
  only in a form that permits inclusion of all files as found in
  the original, archived form in which BNU is distributed.  You are
  not permitted to modify any portion of the package in any way,
  including, but not limited to adding files to or removing files
  from the distribution package, changing or editing the
  documentation, and/or changing or modifying the executable
  program.  Permission is granted to repack the distribution
  archive using a different packing method, provided that the
  uncompressed contents EXACTLY match the uncompressed contents of
  the distribution archive (I have no particular affiliation with
  or preference for any particular archiving method - SEA's ARC is
  used simply because it is the most widely accepted amongst
  archivers at the time this package was distributed).
            
  BNU is not provided with any warranty of any kind, including, but
  not limited to fitness for any particular purpose or
  consequential loss.
  
  This package may be posted for download or file request by any
  FidoNet or compatible network system in archived form, and in
  adherence to the terms of the License above.  No profit may be
  realised directly from such distribution, although BNU may be
  provided for download on "pay systems."  Distribution on diskette
  form is strictly prohibited unless done for free for for a charge
  not exceeding the cost of the diskettes.
  
  COMMERICAL USE:  BNU is provided for commercial use under a
  different licensing arrangments.  Please contact the author by
  netmail at either of the addresses below for details.
  
  
  "ARC" is a trademark of System Enhancement Associates, Inc.
  
  
  ==============================================================
  
  Please direct any enquiries or problem reports via netmail to:
  
  
                 Fidonet  3:632/348
    or   OZ_NET/Alternet  7:833/380.4
  
  
               //    ------------------------    \\
              //-         David Nugent           -\\
              \\\\   Unique Computing Pty Ltd   ////
               //   Fidonet Node 3:632/348.0   \\
               //    ------------------------    \\
  

                                  - 15 -






             BNUCom Rev 5 FOSSIL Communications Driver v1.30A

  
  ==============================================================























































                                  - 16 -