Loading firmware to 6500/6700 printers using Printer Management Utility (PMU)

- Preparation for Printer Microcode Download

  - Download the file from the 6500/6700 Firmware Webpage to the directory of your choosing (typically a temp directory).

  - If you have PMU loaded on your PC, put the microcode in the c:\ibm\pmu directory.  (Note: If you do not have PMU loaded, follow the install instructions in Section 1.2.)

  - To expand the file, double click the file from a Windows Explorer window or type the filename from a DOS command line.  The file will expand to a file with a “PRG” extension.

- Installation of PMU

  - Download and install the latest version of the Printer Management Utility (PMU) from the PMU Webpage.

  - Ensure that you read the readme file for Java requirements and loading instructions.

  - Follow instructions in Readme or PMU Manual for installation.

- Start the PMU program from the Start button (“Programs –> InfoPrint Solutions –> PMU -> Printer Management Utility” is the default path).

- Highlight desired printer.  If the printer is not in the list, it can be manually added

to the list.   Add additional printers please see the Adding a Printer Manually Appendix A

of these instructions.

- Click on Insert a new download file into the database  toolbar button or select

Edit –> Insert –> Download file to add the new file.

- Double Click on New Download File.

- Click Browse, change to the directory where your microcode program file (PRG) is located, highlight the desired microcode.prg file, and click Open.

- Highlight the printer, then select “Applications –> File Download”.

- Determine if you want to overwrite the configuration and flash files when new microcode is downloaded.  To preserve the item, put a check in the box.  (Typically, Flash files will not be present unless a special file has been downloaded to the printer, so select Firmware and Restore Config.)  Once done, click Start.

- Messages will be displayed under the progress box.

- The printer will reboot and the progress will indicate Done when everything  is

complete.

Appendix A

Adding a Printer Manually

- Double click on New_Printer.

- Printer properties box will appear.  Click on connections and type in the desired IP address and click OK.

Appendix B

TROUBLESHOOTING

- If connection to a printer failed it will be indicated by the “ERROR: Could not connect to printer” dialog box.  Review the messages below the dialog box to help in troubleshooting the problem.

- If the error is seen follow these steps:

- Ping the printer - If this fails, follow customer network support protocol.

- Ensure that you can successfully telnet into the printer

Command  - 	telnet x.x.x.x

User  default - root

Password default – no password (blank)

- Ensure DIAGNOSTIC PORT is set to DEBUG ETHERNET.  (Refer to the “Printer Setup” section of the Printer Management Utility Manual.)

- If you still cannot communicate, it may be a network firewall related issue.

Use a PC on the same subnet as the printer to load the code or contact your

network support group.