Version 5.0

README

GSMGPRS Motorola BSS GSR080 v2.1.1.0

Note: Before using this information and the product it supports, read the information in Notices on page 11.

Table of Contents

1	About this Documentation	1

1.1	Audience	1

1.2	Required Skills and Knowledge	1

2	Installation	2

2.1	Pre-requisite Requirement	2

2.2	Technology Pack Package Contents	3

2.3	Gateway Patch Procedure	3

2.4	Technology Pack Patch Installation Procedure	4

3	Defects Fixed	10

Appendix A	Notices and Trademarks	11

# About this Documentation

## Audience

The target audience of this document is IBM Performance Manager for Wireless customers. They should be familiar with telecommunication and IT principles and should also have a good understanding of Solaris.

IMPORTANT: Before attempting an installation of Performance Manager for Wireless you are strongly advised to read the release notes and any readme files distributed with your Performance Manager for Wireless software. Readme files and release notes may contain information specific to your installation not contained in this guide. Failure to consult readme files and release notes may result in a corrupt, incomplete or failed installation.

Note: Performance Manager for Wireless Administrators should not, without prior consultation and agreement from IBM, make any changes to the Index Organized tables or database schema. Changes to the Index Organized tables or database schema may result in corruption of data and failure of the Performance Manager for Wireless System. This applies to all releases of Performance Manager for Wireless using all versions of interfaces.

## Required Skills and Knowledge

This guide assumes you are familiar with the following:

General IT Principles

Sun Solaris Operating System

Oracle Database

Windows operating systems

Graphical User Interfaces

Network Operator's OSS and BSS systems architecture

This guide also assumes that you are familiar with your company’s network and with procedures for configuring, monitoring, and solving problems on your network.

# Installation

## Pre-requisite Requirement

Before installing this technology pack, the following GOM technology pack and GSMGPRS_Motorola_BSS_GSR080 technology pack must be installed.

- vallent-vt-Neutral_Core_GOM-1.0.tar.gz

- vallent-vt-Neutral_GSM_BSS_NSS_GOM-1.0.tar.gz

- vallent-vt-Neutral_GPRS_UMTS_CN_GOM-1.0.tar.gz

- vallent-vt-Neutral_UMTS_UTRAN_GOM-1.0.tar.gz

- vallent-vt-Neutral_GPRS_BSS_GOM-1.0.tar.gz

- vallent-vt-GSMGPRS_Motorola_BSS_GSR080-2.0.0.tar.gz

## Technology Pack Package Contents

This section describes the contents of the technology pack package.

Docs (DOCS/)

- GSMGPRS_Motorola_BSS_GSR080_NA912_README_v2.1.1.0.doc (this file)

- Quick reference guide for deployment of a Technology Pack Patch.

* Note: This document must be used in conjunction with the GSMGPRS_Motorola_BSS_GSR080_NA912_README_v2.0.0.0.doc

- PRS & FS

- Product Requirement Spec and Functional Spec for this Technology Pack Patch.

Technology Pack Package (TECHPACK/)

- vallent-vt-GSMGPRS_Motorola_BSS_GSR080-2.1.1.tar.gz

- Quick reference guide for deployment of a Technology Pack Patch

Gateway Patch File (GATEWAY/)

- UserConfig.pm

- The UserConfig.pm file contains the configurations for the Post Parser stage

## Gateway Patch Procedure

GSMGPRS Motorola BSS GSR080 Gateway Configuration Patch

The gateway configuration patch file for GSMGPRS Motorola BSS GSR080 is:

- UserConfig.pm

Pre-requisite Gateway Framework, Vendor Gateway,  and Gateway Configuration

The GSMGPRS Motorola BSS GSR080 gateway configuration requires the following Gateway Framework, Vendor Gateway and Gateway Configuration.

- vallent-vt-gways-gateway-framework-3.4.0.3.tar.gz

- vallent-vt-gways-generic-csv-3.4.0.1.tar.gz

- vallent-vt-gways-cfg-motorola-bss-3.4.1.2.tar.gz

GSMGPRS Motorola BSS GSR080 Gateway Patch Implementation

  - For GSMGPRS Motorola BSS GSR080 Patch, the Gateway bugs fix only impacted UserConfig.pm file. Before apply this gateway patch, backup the existing UserConfig.pm with a meaningful name.

  - Copy UserConfig.pm from GATEWAY folder to correspond $GATEWAY_DIR/ motorola-bss/gsr8/ directory.

## Technology Pack Patch Installation Procedure

Install the GSMGPRS Motorola BSS GSR080 Technology Pack Patch as follows. This section explains the procedure to install this Technology Pack Patch on a step by step basis. Please read each section and sub-section carefully.

2.4.1 Technology Pack Uninstallation:

1) Uninstall the technology pack using the following command:

techpack_admin –u techpack –n “Motorola GSM BSS”

2) Rename vallent-vt-GSMGPRS_Motorola_BSS_GSR080.remove script to vallent-vt-GSMGPRS_Motorola_BSS_GSR080.remove.backup in /appl/virtuo/admin/software

3) Run the following commands to remove the impacted busyhours:

sbh_admin -d –n BSC_CCH_on_cell_based_Busy_Hour

sbh_admin -d –n BSC_Packet_UL_and_DL_on_cell_based_Busy_Hour

sbh_admin -d –n BSC_TCH_on_cell_based_Busy_Hour

sbh_admin -d –n Cell_CCH_busy_hour

sbh_admin -d –n Cell_Packet_DL_busy_hour

sbh_admin -d –n Cell_Packet_UL_and_DL_busy_hour

sbh_admin -d –n Cell_Packet_UL_busy_hour

sbh_admin -d –n Cell_Packet_max_busy_hour

sbh_admin -d –n Cell_TCH_busy_hour

sbh_admin -d –n Gb_throughput_Busy_hour

sbh_admin -d –n Processor_load_busy_hour

sbh_admin -d –n SS7link_LMTP_MSU_received_busy_hour

sbh_admin -d –n SS7link_LMTP_MSU_transmitted_busy_hour

sbh_admin -d –n SS7link_MTP_MSU_received_busy_hour

sbh_admin -d –n SS7link_MTP_MSU_transmitted_busy_hour

sbh_admin -d –n X25_frames_RX_and_TX_busy_hour

2.4.2 Technology Pack Installation:

4) Copy the technology pack patch, vallent-vt-GSMGPRS_Motorola_BSS_GSR080-2.1.1.tar.gz, to $WMCROOT/admin/techpacks/packages.

5) Execute the following command:

$WMCROOT/admin/common/install/scripts/deploy_techpacks -wmcr /appl/virtuo –techpacks vallent-vt-GSMGPRS_Motorola_BSS_GSR080-2.1.1.tar.gz

6) After deploying the technology pack patch, the patch can be installed using the following command as per installation guide.

techpack_admin –a

7) Go to this path upon completion of technology pack patch installation:

$WMCROOT/admin/techpacks/GSMGPRS_Motorola_BSS_GSR080/2.0.0/loadmaps/GSMGPRS_Motorola_BSS_GSR080

8) Remove the current loadmap in the following sequences. Example of command:

lcm_admin -delete loaderconfiguration_motorola_bss_gsr080.xml

lcm_admin -delete datasource_motorola_bss_gsr080.xml

lcm_admin -delete relations_motorola_bss_gsr080.xml

9) Go to this path:

$WMCROOT/admin/techpacks/GSMGPRS_Motorola_BSS_GSR080/2.1.1/loadmaps/GSMGPRS_Motorola_BSS_GSR080

10) Install a new loadmap with the following command sequence:

lcm_admin -load datasource_motorola_bss_gsr080.xml

lcm_admin -load loaderconfiguration_motorola_bss_gsr080.xml

lcm_admin -load relations_motorola_bss_gsr080.xml

11) Initialize the list of loaders in the system as follows:

sap stop

sapmgr stop

sapmgr start

sap start as

12) Check the latest loaders have been added:

sap disp

13) Execute the following command to start the loader:

sap start loadmotorolagsmbss_gsr80

14) To verify patch result, use the below command. The version tech pack for this patch should

be version 2.1.1.

lcm_admin -list

15) Re-provision SummaryInstance.xml and SummaryInstancePCalcs.xml:

summary_admin –c –f      $WMCROOT/admin/techpacks/GSMGPRS_Motorola_BSS_GSR080/2.1.1/summaries/SummaryInstance.xml

summary_admin –c –f $WMCROOT/admin/techpacks/GSMGPRS_Motorola_BSS_GSR080/2.1.1/summaries/SummaryInstancePCalcs.xml

16) Re-provision BusyHours:

sbh_admin -i -f BusyHourInstance.xml -m overwrite

17) Applying the new Reports:

Go to the reports directory:

cd

$WMCROOT/admin/techpacks/GSMGPRS_Motorola_BSS_GSR080/2.1.1/reports

Run the following command:

report_impexp -i -u sysadm -p Sysadm01 -f . -l /Users/sysadm/ -dup overwrite

  - Please follow the steps below to manually alter the size of the LAPD_ID columns if aforementioned column size in database is VARCHAR2 (50).

- Launch sqlplus by typing:

sqlplus virtuo/Virtuo01@vtdb

- Run the following SQL command in order to alter the column size for some impacted tables:

alter table nc_lapd modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PREEEMP_DBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PREEEMP_DSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PREEEMP_LTM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PREEEMP_MBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PREEEMP_MSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PREEEMP_TAB modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PREEEMP_WBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PREEEMP_WSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PRM_EMRG_DBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PRM_EMRG_DSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PRM_EMRG_LTM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PRM_EMRG_MBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PRM_EMRG_MSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PRM_EMRG_TAB modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PRM_EMRG_WBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_PRM_EMRG_WSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_RES_DBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_RES_DSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_RES_LTM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_RES_MBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_RES_MSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_RES_TAB modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_RES_WBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_RES_WSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_STATUS_DBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_STATUS_DSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_STATUS_LTM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_STATUS_MBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_STATUS_MSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_STATUS_TAB modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_STATUS_WBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_ATER_STATUS_WSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM__DSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM__MSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM__WSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM_DBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM_DSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM_LTM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM_MBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM_MSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM_TAB modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM_WBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_BSS_DAT_TRANSM_WSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_CONGCNTRL_DBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_CONGCNTRL_DSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_CONGCNTRL_LTM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_CONGCNTRL_MBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_CONGCNTRL_MSM modify (LAPD_ID varchar(100));

alter table MOT_LAPD_CONGCNTRL_TAB modify (LAPD_ID varchar(100));

alter table MOT_LAPD_CONGCNTRL_WBH modify (LAPD_ID varchar(100));

alter table MOT_LAPD_CONGCNTRL_WSM modify (LAPD_ID varchar(100));

- To update the data type for MTP_SL_IN_SERVICE column, execute the following command:

alter table MOT_SIGLNK_MTP_C7_PERF_DBH modify (ulo0octahl26secar00hw01qk4 NUMBER);

alter table MOT_SIGLNK_MTP_C7_PERF_DSM modify (ulo0octahl26secar00hw01qk4 NUMBER);

alter table MOT_SIGLNK_MTP_C7_PERF_LTM modify (ulo0octahl26secar00hw01qk4 NUMBER);

alter table MOT_SIGLNK_MTP_C7_PERF_MBH modify (ulo0octahl26secar00hw01qk4 NUMBER);

alter table MOT_SIGLNK_MTP_C7_PERF_MSM modify (ulo0octahl26secar00hw01qk4 NUMBER);

alter table MOT_SIGLNK_MTP_C7_PERF_TAB modify (ulo0octahl26secar00hw01qk4 NUMBER);

alter table MOT_SIGLNK_MTP_C7_PERF_WBH modify (ulo0octahl26secar00hw01qk4 NUMBER);

alter table MOT_SIGLNK_MTP_C7_PERF_WSM modify (ulo0octahl26secar00hw01qk4 NUMBER);

- Commit the changes:

commit;

- Exit the sqlplus by typing:

EXIT

# Defects Fixed

Bugs resolved in GSMGPRS Motorola BSS GSR080 fixpack version 2.1.1.0.

| APAR #/ CR # | Headline |
| --- | --- |
| IZ25709 | MAPPING FOR LACID HARDCODES A SUBSTR OF THE CELLID AS THE LACID IN THE LOADER AND IS INCORRECT |
| IZ31645 | AGGREGATOR TYPE FOR SUMMARY OF INFORMATION_FRAMES_TX_AND_RX IS DIFFERENT AT THE LAPD(SUMMED) AND X25(AVERAGED) OBJECTS. |
| IZ29120 | OUTPUT LIF FILE NAMES ARE NOT UNIQUE CAUSING THE FILES TO BE OVERWRITTEN |
| IZ16668 | THERE IS A MISMATCH BETWEEN THE LOADMAP EXPRESSION AND THE VALUE IN THE LIF |
| IZ22244 | SEVERAL STANDARD SUMMARIES REPORTS ARE NOT WORKING FOR PCALCS IN TNPMW TECH PACKS. |
| IZ27285 | INCORRECT TYPE SPECIFIED FOR COUNTERS |
| IZ16422 | WRONG LOADMAP EXPRESSION FOR KPI - SIGNALLING_LINK.MOTOROLA.GSM.MTP_C7_PERFORMANCE.MTP_SL_IN_SERVIC |
| IZ32623 | GSM_MOTOROLA_BSS_GSR8 TECH PACK MISSING COUNTERS AFTER COMPARING FS AND PRS. |
| IZ37719 | CALL_ASSIGNMENT_REDIRECTION IN MOTOROLA_CELL_GENERAL_HANDOVER_2_RAW TABLE SHOULD BE OF TYPE ACCUMULATION INSTEAD OF INTENSITY |
| valnt00055556 | MPM GSMGPRS Motorola BSS GSR8: To Un-Store-Raw 30 KPIs |
| valnt00059958 | rsl_statistics lif file has been moved to bad directory |

Notices and Trademarks

This appendix contains the following:

Notices

Trademarks

#### Notices

This information was developed for products and services offered in the U.S.A.

IBM may not offer the products, services, or features discussed in this document in other countries. Consult your local IBM representative for information on the products and services currently available in your area. Any reference to an IBM product, program, or service is not intended to state or imply that only that IBM product, program, or service may be used. Any functionally equivalent product, program, or service that does not infringe any IBM intellectual property right may be used instead. However, it is the user's responsibility to evaluate and verify the operation of any non-IBM product, program, or service.

IBM may have patents or pending patent applications covering subject matter described in this document. The furnishing of this document does not grant you any license to these patents. You can send license inquiries, in writing, to:

IBM Director of Licensing
IBM Corporation
North Castle Drive
Armonk NY 10504-1785
U.S.A.

For license inquiries regarding double-byte (DBCS) information, contact the IBM Intellectual Property Department in your country or send inquiries, in writing, to:

IBM World Trade Asia Corporation
Licensing
2-31 Roppongi 3-chome
Minato-ku
Tokyo 106-0032
Japan.

The following paragraph does not apply to the United Kingdom or any other country where such provisions are inconsistent with local law: INTERNATIONAL BUSINESS MACHINES CORPORATION PROVIDES THIS PUBLICATION “AS IS” WITHOUT WARRANTY OF ANY KIND, EITHER EXPRESS OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF NON-INFRINGEMENT, MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE. Some states do not allow disclaimer of express or implied warranties in certain transactions, therefore, this statement may not apply to you.

This information could include technical inaccuracies or typographical errors. Changes are periodically made to the information herein; these changes will be incorporated in new editions of the publication. IBM may make improvements and/or changes in the product(s) and/or the program(s) described in this publication at any time without notice.

Any references in this information to non-IBM Web sites are provided for convenience only and do not in any manner serve as an endorsement of those Web sites. The materials at those Web sites are not part of the materials for this IBM product and use of those Web sites is at your own risk.

IBM may use or distribute any of the information you supply in any way it believes appropriate without incurring any obligation to you.

Licensees of this program who wish to have information about it for the purpose of enabling: (i) the exchange of information between independently created programs and other programs (including this one) and (ii) the mutual use of the information which has been exchanged, should contact:

IBM Corporation
5300 Cork Airport Business Park
Kinsale Road
Cork
Ireland.

Such information may be available, subject to appropriate terms and conditions, including in some cases, payment of a fee.

The licensed program described in this document and all licensed material available for it are provided by IBM under terms of the IBM Customer Agreement, IBM International Program License Agreement or any equivalent agreement between us.

Information concerning non-IBM products was obtained from the suppliers of those products, their published announcements or other publicly available sources. IBM has not tested those products and cannot confirm the accuracy of performance, compatibility or any other claims related to non-IBM products. Questions on the capabilities of non-IBM products should be addressed to the suppliers of those products.

All statements regarding IBM's future direction or intent are subject to change or withdrawal without notice, and represent goals and objectives only.

This information contains examples of data and reports used in daily business operations. To illustrate them as completely as possible, the examples include the names of individuals, companies, brands, and products. All of these names are fictitious and any similarity to the names and addresses used by an actual business enterprise is entirely coincidental.

If you are viewing this information softcopy, the photographs and color illustrations may not appear.

#### Trademarks

IBM, IBM logo, Tivoli, and Netcool are trademarks of International Business Machines Corporation in the United States, other countries or both.

Adobe, the Adobe logo, PostScript, and the PostScript logo are either registered trademarks or trademarks of Adobe Systems Incorporated in the United States, and/or other countries.

Java and all Java-based trademarks and logos are trademarks of Sun Microsystems, Inc. in the United States, other countries, or both.

Microsoft, Windows, Windows NT, and the Windows logo are trademarks of Microsoft Corporation in the United States, other countries, or both.

UNIX is a registered trademark of The Open Group in the United States and other countries.

Intel and Pentium are trademarks or registered trademarks of Intel Corporation or its subsidiaries in the United States and other countries.

Other company, product or service names may be trademarks or service marks of others.

IBM

# Text boxes

© Copyright IBM Corporation 2008

International Business Machines Corporation

5300 Cork Airport

Business Park

Kinsale Road

Cork

Ireland

Printed in the Republic of Ireland

All Rights Reserved

IBM, IBM logo, Tivoli, and Netcool are trademarks of International Business Machines Corporation in the United States, other countries or both.

Other company, product and service names may be trademarks or service marks of others.

IBM